## Slide 1: RaLaZaBa Electonics Oral Representation
Ali Aydın
Anıl Aydın
Enes Ayaz
Nail Tosun
Selman Dinç

## Slide 2: Team
Ali Aydın
Anıl Aydın
Nail Tosun
Selman Dinç
Enes Ayaz

## Slide 3: Outline
Team Definition
Objectives, Functional Requirement and Problem Statement
Overall Solution
Decision and Control Unit
Environment Sensing Unit, Motion of the Sensing Unit
Motion, Mapping and Self localization Units
Solution Approach and Test Results
Deliverables, Time Plan and Cost Analysis

## Slide 4
Chart: 
| Power Electronics | Electronics
 | 3 | 2
Chart: 
| Power Electronics | Electronics | Control | Computer | Microwave and Antenna
 | 3 | 3 | 1 | 2 | 1
Team
EE Options Including Minors
EE Options Majors

## Slide 5
Selman Dinç
Project Manager
Enes Ayaz
Software Engineer
Ali Aydın
Hardware Engineer
Nail Tosun
System Engineer
Anıl Aydın
Software Engineer
Team

## Slide 6
Objectives
Performance
Accuracy
Operation Time
Marketable
Cost
Ease of Use
Robustness
Power Consumption
0.2
0.2
0.18
0.16
0.16
0.1
Order of Importance
Objective Tree

## Slide 7
 | Short Operation Time | Accuracy | Low Cost | Ease of use | Robust operation with changing environment | Low power consumption
3 | <5 min | Understand how many objects are in field, their shapes properly and determine their positions correctly | <50 $ | User friendly GUI and live mapping | Works properly in laboratory and fair field for both dark and sunlight conditions | <10 W
2 | 5-10 min | Understand how many objects are in field and their shapes properly, but cannot determine their positions correctly | 50-150 $ | User friendly GUI but long update duration of data | Works in laboratory everywhere but sometimes cannot operate properly on fair field ground | 10-20 W
1 | 10-15 min | Understand how many objects are in field but cannot determine their position and shapes correctly | 150-200 $ | User friendly GUI presenting data transmission at the end of operation | Works only at specific conditions in laboratory | 20-50 W
0 | >15 min | Number of objects, their shapes and their position cannot be determined correctly | >200 $ | No user-friendly GUI and no real time data processing | Sometimes works, but sometime does not work in any condition | >50 W

## Slide 8
Functional Requirements

## Slide 9
Problem Statement

## Slide 10: How do we need a way to improve solutions?

## Slide 11: How do we make a distribution of duties?
We seperate the device into 7 subsytems.
Decision and Control Unit
Environment Sensing Unit
Motion of sensor
Motion Unit
Mapping
Sensing Unit for Self Localization
Power Unit

## Slide 12: Decision and Control Unit
The unit is like brain of the devices.
It governs all of other subsytems.
The unit is divided in two basic operation.
1) Control systems
2) Decision systems

## Slide 13: Operations
Trigger

## Slide 14: Algorithms in Decision and Control Unit
Mapping Algorithm:
Shape Finder Algorithm:
Road Map Algorithm:

## Slide 15: Mapping Algorithm
As seen , there are some points that the device makes the measurement.
Direction of the device changes.
Position of the device changes.
  Two data group are received.
  The data are merged by algorithm to create map.

## Slide 16: Solution
Direction of the devices are converted to stationary cooradinates.
Vector addition is made.
Self position and measurement are merged.
Rotation Matrix
Vector Addition

## Slide 17: Road Map Algorithm
  There is a uncompleted map and
  create a roadmap.
  A destination point are created
  to control the actuator.
SLAM
  A map is required for localization
  A localization is required for map
  Like chicken-egg problem.
  Actually, it is a probabilistic model.

## Slide 19: Environment Sensing Unit

## Slide 20: Motion Of Sensing Unit
Rotate 90 degree clockwise or counter-clock wise

## Slide 21: Motion Unit
Differential drive technique with freewheel.

## Slide 22: Mapping Unit
Object types
Position of object center
How many objects there are in the field
Map of field

## Slide 23: Sensing Unit For Self-localization
We need to determine the position of the device to refer the mesurements.
We could not rely on encoders on the motors only.

## Slide 24
Skidding.
Spinning.

## Slide 25: Our Solution: A Trackball Mouse
Key features of a typical mouse:
400 step per inch resolution
It can detect without error up to 12 inches per second
What is inside a trackball mouse?

## Slide 26: How Are We Going To Use Them?
Using one mouse gives us linear motion on a plane, not angular motion.
If we use two of them, we can determine our heading.

## Slide 28
With two mouse we coud determine our position via the followings:
dX = (dX1 + dX2)/2
dY = (dY1 + dY2)/2
ϴ = arctan((dY1-dY2)/(dX1-dX2))

## Slide 29: Power Unit
Without constant supply of energy our device is a garbage!
The power mainly consumed for actuation.
With rough estimation, we need
1A for 2 actuators in motion unit,
1A for actuator of sensing unit,
1A for computation and sensing

## Slide 30
Mechanical Structure

## Slide 31: Testing Our Conceptual Idea
We took some meauremetns with real data of objects.

## Slide 32: How did we take data?
The test setup using VL53L0X and servo.
We took three different measurements of a cylinder with radius of 10 cm.
Then, we gathered the data via MATLAB.

## Slide 33: Test Setup for Sensing Unit and Results
Test Map and its output for cylinderical object

## Slide 34: Additional Tests For Sensing Unit
Test Map and its output for triangular object.

## Slide 35: Additional Tests For Sensing Unit
Test Map and its output for rectangular objects

## Slide 36: Shape Finder Algorithm and Tests
Get (x,y) Coordinate Information
Convert coordinates to 2D array
Make preprocessing
Convert to gray scale
Blur the gray image
Find edges using Canny Edge Detector
Dilate and erode the edged image
Find all contours on the image
Specify area range considering objects in the environment
Find number of sides of each contour
#of sides = 3
#of sides = 4
#of sides > 4
Output: triangle
Find center
Output: Rectangle
Find center
Output: Cylinder
Find center

## Slide 38: Additional Tests For Shape-finder Unit

## Slide 39: Additional Tests For Shape-finder Unit

## Slide 40: Deliverables
Equipment
  The mapping device
  Platform
  Battery and charging unit
Software
  User Interface
Documents
  User Manual
Technical Support

## Slide 41: Time Plan
April
March
February
January
Tests for Subsystems
Integration of Subsystems And Prototype Production
Tests for overall system and improvements of the system
May
Delivery of the Product
Improvements of Subsystems and Detailed Design

## Slide 42: Cost Analysis
117 $

## Slide 43: Thank You For Listening